## Slide 1: HDDS1104 Operating Systems and Networking
Topic 05 Introduction to Computer Networking

## Slide 2: Intended Learning Outcomes
Describe services provided in a computer network
Discuss different network topologies and technologies
Describe the OSI reference model
List relevant protocols involved in TCP/IP model
Explain network security and protection issues

## Slide 3: What is computer network?

## Slide 4: What is computer network?
a group of computers that
  use a set of common communication protocols over digital interconnections
  for the purpose of sharing resources located on or provided by the network nodes.
Including
  personal computers, servers, networking hardware, or other specialized or general-purpose hosts.
identified by hostnames and network addresses.

## Slide 5: Services of Computer Networks
Helps you to share resource such as printers
Allows you to share expensive software's and database among network participants
Provides fast and effective communication from one computer to another computer
Helps you to exchange data and information among users via a network

## Slide 6: Function of computer network
Shared data - Shared data are data that file servers provide to clients such as data files, printer access programs and e-mail.
Shared printers and other peripherals - Shared printers and peripherals are hardware resources provided to the users of the network by servers.

## Slide 7: Network devices

## Slide 8: Servers
computers that hold shared files, programs, and the network operating system.
provide access to network resources to all the users of the network.
Examples
  File servers, print servers, mail servers, communication servers, database servers, fax servers and web servers

## Slide 9: Clients
Clients are computers that access and use the network and shared network resources.
Traditional model
  Client/Server
    Client request service,
    Server respond with resource
  Peer-to-peer
    Peer nodes serve as both clients & servers to other nodes.

## Slide 10: Transmission Media
facilities used to interconnect computers in a network,
such as
  twisted-pair wire,
  coaxial cable, and
  optical fiber cable.

## Slide 11: Network Interface Card (NIC)
a special expansion card / port in each computer
Functions
  prepares (formats) and sends data,
  receives data, and
  controls data flow between the computer and the network.

## Slide 12: Hub
a device that splits a network connection into multiple computers.
Each computer in the network should then figure out whether the broadcast data is for them or not.

## Slide 13: Switch
a telecommunication device grouped as one of computer network components.
Switch is like a Hub but built in with advanced features.
It uses physical device addresses in each incoming messages so that it can deliver the message to the right destination or port.

## Slide 14: Router
device that used to connect a LAN with an internet connection
have two distinct networks (LANs) or want to share a single internet connection to multiple computers, we use a Router.
Types of Router:
  wired
  wireless.
choice depends on physical setting, speed and cost.

## Slide 15: Cisco Packet Tracer
a tool that allows you to simulate real networks. It provides three main menus that allow you to:
  add devices and connect them via cables or wireless
  select, delete, inspect, label, and group components within your network
  manage your network
may sign up and download version 8.2.0 or latest version in the following URL:
https://www.netacad.com/about-networking-academy/packet-tracer/

## Slide 16: Exercise – Launching Cisco Packet Tracer
Start Cisco Packet Tracer
Add the following devices
  End Devices:
    PC, Server
  Network Devices:
    Router, Switch, Hub

## Slide 17: Categories of networks

## Slide 18: Categories of networks
can be categorized by their size.
A computer network is mainly of four types:
  PAN(Personal Area Network)
  LAN(Local Area Network)
  MAN(Metropolitan Area Network)
  WAN(Wide Area Network)

## Slide 19: PAN (Personal Area Network)
used for connecting the computer devices of personal use
Personal computer devices that are used
  laptop, mobile phones, media player and play stations.
Types of Personal Area Network
  Wired Personal Area Network: created by using the USB
  Wireless Personal Area Network: such as WiFi, Bluetooth

## Slide 20: LAN (Local Area Network)
a group of computers connected to each other in a small area such as building, office.
used for connecting two or more personal computers through a communication medium such as twisted pair, coaxial cable, etc.
less costly as it is built with inexpensive hardware
  such as hubs, network adapters, and Ethernet cables.
Example:
  Home Wi-Fi networks and
  small business networks

## Slide 21: MAN (Metropolitan Area Network)
Covers a larger geographic area
  by interconnecting a different LAN to form a larger network.
Government agencies use MAN to connect to the citizens and private industries.
It has a higher range than Local Area Network (LAN).

## Slide 22: WAN (Wide Area Network)
Extends over a large geographical area such as states or countries.
biggest WAN in the world
  The internet
widely used in the field of Business, government, and education.

## Slide 23: Examples of Wide Area Network:
Mobile Broadband:
  A 4G network is widely used across a region or country.
Last mile:
  A telecom company is used to provide the internet services to the customers in hundreds of cities by connecting their home with fiber

## Slide 24: Network topologies

## Slide 25: Physical network topologies
Examples
  Point to point topology
  Point to multipoint topology
  Bus Topology
  Ring Topology
  Star Topology
  Mesh Topology
  Hybrid Topology
Network topologies describe the methods in which all the elements of a network are mapped.

## Slide 26: Point to point topology
point to point topology connects any two points (devices) in a network.

## Slide 27: Point to multipoint topology
connects one to many points.
provides multiple paths from a single device to multiple devices.

## Slide 28: Bus Topology
uses a single cable which connects all the included nodes.
The main cable acts as a spine for the entire network.
One of the computers in the network acts as the computer server.

## Slide 29: Ring Topology
every device has exactly two neighboring devices for communication purpose.
its formation is like a ring.
every computer is connected to another computer.
the last node is combined with a first one.

## Slide 30: Star Topology
All the computers connect with the help of a hub.
This hub is called a central node,
all other nodes are connected using this central node.

## Slide 31: Mesh Topology
It develops a P2P (point-to-point) connection between all the devices of the network.
It offers a high level of redundancy, so even if one network cable fails, still data has an alternative path to reach its destination.

## Slide 32: Hybrid Topology
Hybrid topology combines two or more topologies.

## Slide 33: How to select a Network Topology?
Here are some important considerations for selecting the best topology to create a network in your organization:
  Bus topology is surely least expensive to install a network.
  If you want to use a shorter cable or planning to expand the network in future, then star topology is the best choice for you.
  Fully mesh topology is theoretically an ideal choice as every device is connected to every other device.
  If you want to use twisted pair cable for networking, then you should build star topologies.

## Slide 34: Exercise – Star Network & Ring Network
Use Cisco packet tracer to build a start & a ring network
Only server support 2 NICs

## Slide 35: Signalling and Encoding

## Slide 36: Transmission Modes
the mechanism of transferring of data between two devices connected over a network.
also called Communication Mode.
Types of transmission modes
  Simplex Mode
  Half duplex Mode
  Full duplex Mode

## Slide 37: SIMPLEX Mode
data can be sent only in one direction.
Examples
  loudspeakers,
  television broadcasting,
  television and remote,
  keyboard and monitor etc.

## Slide 38: HALF DUPLEX Mode
data can be transmitted in both directions on a signal carrier, but not at the same time.
Example of half duplex is a walkie- talkie in which message is sent one at a time but messages are sent in both the directions.

## Slide 39: FULL DUPLEX Mode
We can send data in both the directions as it is bidirectional at the same time in other words, data can be sent in both directions simultaneously.
Example of Full Duplex is a Telephone Network in which there is communication between two persons by a telephone line, using which both can talk and listen at the same time.

## Slide 40: Signaling and Encoding
Signaling is the method by which you define what a one or zero is.
Encoding is how you use the 1s and 0s to represent information.
Decoding is the reverse process of encoding which is to extract the information from the converted format.

## Slide 41: Transmission of digital data
Data transmission (data communications) is the transfer and reception of data (a digital bit-stream or a digitized analog signal) over a point-to-point or point-to-multipoint communication channel.

## Slide 42: Open Systems Interconnection (OSI) Model

## Slide 43: Computer Network Models: Layered Architecture
main aim
  to divide the design into small pieces.
Each lower layer adds its services to the higher layer
  to provide a full set of services to manage communications and run the applications.
ensures the independence between layers
  by providing the services from lower to higher layer
  without defining how the services are implemented.
any modification in a layer will not affect the other layers.

## Slide 44: Open Systems Interconnection (OSI) Model
Reference conceptual model
Communications split in 7 abstraction layers
  1. Physical
  2. Data Link
  3. Network
  4. Transport
  5. Session
  6. Presentation
  7. Application

## Slide 45: OSI Model

## Slide 46: Functions of layers

## Slide 47: Transmission Control Protocol/Internet Protocol (TCP/IP) model

## Slide 48: Internet protocol suite (TCP/IP)
Set of communication protocols used on the Internet & similar computer networks
Current foundational protocol
  Transmission Control Protocol (TCP)
  Internet Protocol (IP)
  User Datagram Protocol (UDP)

## Slide 49: Internet Protocol Data Flow
Application Layer
Transport Layer
Network Layer
Data-Link Layer
Application Layer
Transport Layer
Network Layer
Data-Link Layer
Network Layer
Data-Link Layer
Network Layer
Data-Link Layer
Internet

## Slide 50: Protocols involved
Application layer
  HTTP, HTTPS, FTP, SMTP, POP3
Transport layer
  TCP, UDP
Network layer
  IPv4, IPv6
Data-link layer
  PPP
  ARP, RARP,
  Wi-Fi, Ethernet
Notes: HTTP Hypertext Transfer Protocol
Simple Mail Transfer Protocol
Post Office Protocol
UDP: User Datagram protocol
PPP
Point-to-Point Protocol
ARP
Address Resolution Protocol
Reverse Address Resolution Protocol

## Slide 51: Transmission Control Protocol
Provides reliable, ordered, and error-checked delivery of a stream of bytes
between applications running on hosts communicating via an IP network
Connection-oriented
Typical ports for applications
  WWW - 80
  Email - 25
  FTP - 21

## Slide 52: Internet Protocol
Network layer communication protocol
Relaying datagram across network boundaries
Delivering packets
  From source host
  To the destination host
Using IP Address

## Slide 53: IP Address
A numeric label used for network interface identification and location addressing
Each network interface has a unique IP address inside a network
IPv4
  A 32-bit number
  E.g.: 192.0.2.1
IPv6
  128-bit number
  E.g.: 2001:db8:0:1234:0:567:8:1

## Slide 54: Domain Name System (DNS)
Hierarchical & decentralized naming system
used to identify computers reachable through the Internet
Commonly used to
  Map human-friendly domain names
  To the numerical IP address
Example
  www.gmail.com (DNS) -> 142.251.220.69 (IP)

## Slide 55: Data-link layer
Lowest layer in the TCP/IP suite
Link
  Physical & logical network components used to interconnect hosts / nodes in the network
Link protocol
  Methods & standards that operate only between adjacent network nodes of a network segment
Example
  Ethernet, Wi-Fi, PPP

## Slide 56: Exercise – Checking Windows Network Setting
Check the [Network Connections] inside windows 10/11.
Check the version of TCP/IP in use
Check the IP of your computer

## Slide 57: Checking network status – Windows 10
May need Administrative right
  Do it at home
Control Panel
  Network & Internet
Status
  Change Network Adapter

## Slide 58: Checking network status -
Search for ‘cmd’
  cmd: Command Prompt of windows
Type ‘ipconfig /all’
  Show all network setting

## Slide 59: Encapsulation of application data
Source: https://en.wikipedia.org/wiki/Internet_Protocol#/media/File:UDP_encapsulation.svg

## Slide 60: Network threats

## Slide 61: Network security: Security threat
Denial of Service (DoS) attack
Distributed DoS attack
Man in the middle
Social engineering
Virus
Worms
Phishing

## Slide 62: Denial of Service (DoS) attack
overwhelms the network host with the stream of bogus data which keep it to process the designed data.
Image source: (Schuba et al, 1997) Analysis of a Denial of Service Attack on TCP

## Slide 63: Distributed DoS attack
attacking an online service or a website by the huge amount of traffic coming from various sources and thus leading to the interruption of the services or even shutting down the network

## Slide 64: Man in the middle
occurs when the person keep a logical connection or equipment between 2 communicating parties.

## Slide 65: Social Engineering
It may comprise of false sites that ask for the information from the unsuspecting web surfers.
Example
  Phishing

## Slide 66: What is phishing?
A form of social engineering
  Deceive people into revealing sensitive information
  Installing malware
Phishing email
https://www.youtube.com/watch?v=48yZUVPacrk&t=13s

## Slide 67: Virus
the program which can infect the computer and copy itself without user knowledge.

## Slide 68: Worm
it is just a program and just not an infestation.
will use a computer network to send worm copies to the other computers without the user's knowledge.

## Slide 69: Network security and mitigation techniques

## Slide 70: Mitigation techniques
Goals of information security
Availability Control
  Access Control
  Authentication
  Encryption
Other mitigation techniques

## Slide 71: Goals of information security - prevent
Loss of Availability
Loss of Integrity
Loss of Confidentiality
Availability
Integrity
Confidentiality
C.I.A Approach
Notes: Reference Reading:
Darril Gibson (2011). SSCP Systems Security Certified Practitioner All-in-One Exam Guide. McGraw-Hill

## Slide 72: Availability
Ensure I.T. systems & data are available when needed
No timeframe
  Mon to Fri / 9 to 5
  24 / 7
Loss of availability
  Data become corrupt
  Server fails

## Slide 73: Integrity
Prevents any unauthorized or unwanted modification of data
Ensure data
  Correct
  Current

## Slide 74: Confidentiality
Ensuring that data is not disclosed to unauthorized users.
Methods
  Authentication
  Access Control
  Encryption

## Slide 75: Security Mechanisms in TCP/IP
Ensure Confidentiality & Integrity
  Public Key Encryption
  Digital Certificates for confidentiality
  Secure Sockets Layer (SSL)
  Transport Layer Security (TLS)

## Slide 76: Other mitigation techniques
Training and awareness
Patch management
Policies and procedures
Incident response