## Slide 1: HDDS1104 Operating Systems and Networking
Topic 7b - IP, Routing

## Slide 2: Intended Learning Outcomes
Explain the Internet Protocol
Explain the principles of Routing
Apply TCP/IP knowledge for simulation in Cisco Packet tracer

## Slide 3: Network Layer (OSI)
Provides
  Inter-networking function (IP)
    Packet Forward
  Congestion Control function: TCP Layer
  Routing function (IP)

## Slide 4: Internet Protocol (IP)
Network layer communication protocol
  Relaying datagram across network boundaries
Routing function
  Inter-networking
TCP/IP
  Connectionless datagram service to TCP

## Slide 5: Encapsulation of application data (Recall from Topic 5)
Source: https://en.wikipedia.org/wiki/Internet_Protocol#/media/File:UDP_encapsulation.svg
Packet
Frame
Datagram /
Segment

## Slide 6: Routing Algorithms

## Slide 7: Routing
Graph abstraction
Distance Vector vs Link State
Dijkstra's Algorithm
Bellman-Ford Algorithm

## Slide 8: Graph Notation
Graph of nodes (N) & edge (E)
N (in networking) = Routers
E (in Networking) = Links
C(s, d): Cost from source (s) to destination (d)
Cost of path
Undirected graph: Symmetric cost
Goal: Find the least cost path

## Slide 9: Graph of Network
N = {u, v, w, x, y, z}
E = {(u,v), (u, x), (u, w), (v, x), (v, w), (x, w), (x,y), (w,y), (w,z), (y,z)}
u
v
w
x
y
z
5
2
2
2
1
1
1
5
3
3

## Slide 10: Distance Vector
Distance Vector
  Vector of distances to all nodes,
    e.g.: u: {u:0, v:2, w:5, x:1, y:2, z:4}
  Sent to neighbors,
    e.g.: u will send to v, w, x
  Large vectors to small # of nodes
    Tell about the world to neighbors
  Older method. Used in Routing Information Protocol (RIP).
u
v
w
x
y
z
5
2
2
2
1
1
1
5
3
3

## Slide 11: Link State
Vector of link cost to neighbors
  Example: u: {v:2, w:5, x:1}
Sent to all nodes,
  Example u will send to v, w, x, y, z
Small vectors to large # of nodes
  Tell about the neighbors to the world
Newer method. Used in Open Shortest Path First (OSPF).
u
v
w
x
y
z
5
2
2
2
1
1
1
5
3
3

## Slide 12: Dijkstra's algorithm
Goal: Find the least cost paths from a given node to all other nodes in the network
Notation:
  c(i,j) = Link cost from i to j if i and j are connected
  D(k) = Total path cost from s to k
  N’ = Set of nodes so far for which the least cost path is known
Method:
Initialize: , D(v) = c(u,v) for all neighbors of u
Repeat until includes all nodes:
  Find node , whose D(w) is minimum
  Add w to
https://en.wikipedia.org/wiki/Dijkstra%27s_algorithm

## Slide 13: Example
N' | D(v) | D(w) | D(x) | D(y) | D(z)
 | 2 | 5 | 1 |  | 
 |  | 4 |  | 2 | 
 |  | 3 |  |  | 4
 | 2 | 3 | 1 | 2 | 4
N' | D(v) | D(w) | D(x) | D(y) | D(z)
 | 2 | 5 | 1 |  | 
 |  | 4 |  | 2 | 
 |  | 3 |  |  | 4
 | 2 | 3 | 1 | 2 | 4
u
v
w
x
y
z
5
2
2
2
1
1
1
5
3
3

## Slide 14: Dijkstra Algorithm
By Ibmua - Work by uploader., Public Domain, https://commons.wikimedia.org/w/index.php?curid=6282617
Notes: By Ibmua - Work by uploader., Public Domain, https://commons.wikimedia.org/w/index.php?curid=6282617

## Slide 15: Bellman-Ford Algorithm
Notation:
  u = Source node
  c(i,j) = link cost from i to j
  h = Number of hops being considered
  = Cost of h-hop path from u to n
Method:
  Initialize:
  For each node,
  If any costs change,
    repeat step 2

## Slide 16: Example of Bellman-Ford Algorithm
0
5
2
2
2
1
1
1
5
3
3
0
5
2
2
2
1
1
1
5
3
3
0
5
2
2
2
1
1
1
5
3
3
0
5
2
2
2
1
1
1
5
3
3

## Slide 17: Autonomous Systems (AS)
An internet connected by homogeneous routers under the administrative control of a single entity
  Presents a common & clearly defined routing policy to the internet
Single Entity
  (Typically) Internet Service Provider (ISP)

## Slide 18: Autonomous System - Example

## Slide 19: Routing Protocols
Interior Router Protocol (IRP):
  Used for passing routing information among routers internal to an autonomous system.
  Also known as IGP.
  Examples: RIP, OSPF, IGRP
Exterior Router Protocol (ERP):
  Used for passing routing information among routers between autonomous systems.
  Also known as EGP.
  Examples: EGP, BGP, IDRP
  Note: EGP is a class as well as an instance in that class.

## Slide 20: Open Shortest Path First (OSPF)
Uses true metrics (not just hop count)
Uses subnet masks
Allows load balancing across equal-cost paths
Supports type of service (ToS)
Allows external routes (routes learnt from other autonomous systems)
Authenticates route exchanges
Quick convergence
Direct support for multicast
Link state routing ⇒Each router broadcasts its connectivity with neighbors to entire network

## Slide 21: Border Gateway Protocol
Inter-autonomous system protocol [RFC 1267]
  Used since 1989 but not extensively until recently
Runs on TCP (segmentation, reliable transmission)
Advertises all transit ASs on the path to a destination address
A router may receive multiple paths to a destination
  Can choose the best path
iBGP used to forward paths inside the AS.
eBGP used to exchange paths between ASs.

## Slide 22: Command – tracert / traceroute
Trace Route: Trace the path of IP
  Windows: tracert
  Mac: traceroute
Use varying IP Time-To-Live (TTL)
  Router decrease TTL by 1
    TTL as hop counter
    TTL = 0 => “Time exceeded”
https://support.microsoft.com/en-us/topic/how-to-use-tracert-to-troubleshoot-tcp-ip-problems-in-windows-e643d72b-2f4f-cdd6-09a0-fd2989c7ca8e

## Slide 23: Tracert Example
tracert www.gmail.com
Tracing route to www.gmail.com [142.250.204.133]
over a maximum of 30 hops:
1 1 ms 1 ms 1 ms homerouter.cpe [192.168.8.1]
2 * * * Request timed out.
3 38 ms 38 ms 63 ms 192.168.245.33
4 29 ms 28 ms 27 ms 10.161.233.48
5 39 ms 28 ms 15 ms wtsam031225.netvigator.com [203.198.13.225]
6 32 ms 37 ms 22 ms 10.195.41.9
7 19 ms 36 ms 47 ms 10.195.41.42
8 * * * Request timed out.
9 33 ms 27 ms 47 ms 72.14.219.16
10 35 ms 28 ms 40 ms 142.250.61.133
11 40 ms 28 ms 14 ms 209.85.240.235
12 18 ms 18 ms 18 ms hkg07s41-in-f5.1e100.net [142.250.204.133]
Trace complete.